Response to CISPR/I/257/CD

| Date | Document | Project Nr. |
| --- | --- | --- |
|  | CISPR/I/257/CD | CISPR 22 am3 f1 Ed. 5.0 |

| National Committee | Line number | Clause/ Subclause | Paragraph Figure/ Table | Type of comment (General/ Technical/Editorial) | COMMENTS | Proposed change | OBSERVATIONS OF THE SECRETARIAT on each comment submitted |
| --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | 9.7.2 | e) | Technical | The text states that: “The longitudinal conversion loss (LCL) of the ISN input (EUT side) shall be 24dB ± 1dB”. This is not representative of the 99% fractile of all networks LCL and will not provide the same protection of radioservices which is provided by the AMN method. | Change to “The longitudinal conversion loss (LCL) of the ISN input (EUT side) shall be 6dB ± 1dB”. |  |
|  |  | 9.7.2 | g) | Technical | The text states that: “If a voltage port on the ISN is available the accuracy of the voltage division factor shall be within ±1,0dB of the nominal value (of -1dB for LCL = 24dB).” This is not representative of the 99% fractile of all networks LCL and will not provide the same protection of radioservices which is provided by the AMN method. | Change to: “If a voltage port on the ISN is available the accuracy of the voltage division factor shall be within ±1,0dB of the nominal value (of -1dB for LCL = 6dB). |  |
|  |  |  |  | General | CISPR S and CISPR Plenary instructed the CISPR I PT to prepare the amendment with the strict objective of providing the same protection for radio services as provided by the present published edition of CISPR22. This instruction seems not to have been followed. | Prepare the amendment in compliance with the instruction. |  |

# Text boxes

FORM COMMENTS (IEC)
2007-03-07